## Slide 1: Routing Protocols
Akshad Vivek Gajbhiye - 2203101
Atharva Sachin Keny - 2204219
Link-State and Distance-Vector
2203107 - Ishita Partha Chail
2203119 - Mrunmayi Sandip Kulkarni

## Slide 2: What is Distance-Vector?

## Slide 3: Distance-Vector Routing
In these protocols, each router does not possess information about the full network topology.
It advertises its distance value (DV) calculated to other routers and receives similar advertisements from other routers unless changes are done in the local network or by neighbours (routers).
Ft Bellman-Ford algorithm

## Slide 4: Information Kept by Distance Vector Router
Each Router has an ID
Associated with each link connected to a router, there is a link cost.
Intermediate hops
Distance Vector Table Initialization
Distance to itself = 0
Distance to all other Router = ∞
Distance Vector Algorithm
A router transmits its distance vector to each of its neighbors in a routing packet.
Each router receives and saves the most recently received distance vector from each of its neighbors.
A router recalculates its distance vector when: It receives a distance vector from a neighbor containing different information than before or It discovers that a link to a neighbor has gone down.
Information Kept by Distance Vector Router
When a node x receives new DV estimate from any neighbor v, it saves v’s distance vector and it updates its own DV using B-F equation:
Dx(y) = min { C(x,v) + Dv(y), Dx(y) }

## Slide 5: The oldest routing protocol, and the oldest distance-vector protocol, is version 1 of the Routing Information Protocol (RIPv1). RIPv1 was formally standardized in 1988. It establishes the shortest path across a network purely on the basis of the hops, that is numbers of routers that need to be passed to reach the destination network. RIP is an interior gateway protocol, so it can be used in local area networks (LANs) on interior or border routers.
FACTS
https://en.wikipedia.org/wiki/Distance-vector_routing_protocol

## Slide 6: What is Link-State?

## Slide 7: Link-State Routing
The basic concept of link-state routing is that every node constructs a map of the connectivity to the network, in the form of a graph, showing which nodes are connected to which other nodes.
Each node then independently calculates the next best logical path from it to every possible destination in the network. Each collection of best paths will then form each node's routing table.
Ft Dijkstra's algorithm
Global View

## Slide 8: keys to understand the link state routing
3
Knowledge about the neighborhood: Instead of sending its routing table, a router sends the information about its neighborhood only. A router broadcast its identities and cost of the directly attached links to other routers.
Flooding: Each router sends the information to every other router on the internetwork except its neighbors. This process is known as flooding. Every router that receives the packet sends the copies to all the neighbors. Finally each and every router receives a copy of the same information.
Information Sharing: A router send the information to every other router only when the change occurs in the information.
https://www.geeksforgeeks.org/unicast-routing-link-state-routing/

## Slide 9
Cisco Press
“There are two link-state routing protocols, OSPF and IS-IS, in use. OSPF being the most popular implementation.”

## Slide 10
We will go in more detail of
“Link State!”
Algorithm
Code
Flooding
Link Break

## Slide 11: Dijkstra’s Algorithm
Implementation of Dijkstra’s Algorithm :
-an example
7
4
2
2
3
8
6
1
What is the Best
Path from
A to F ?
  Graph
  G = (Nodes, Edges)
  Nodes /Routers
  {A,B,C,D,E,F}
  Edges /Links
  {(A,B),(A,C),(B,C),(C,D),(B,D),(C,E),(D,E),(D,F)}

## Slide 12
Step | Visited | D(B)P(B) | D(C)P(C) | D(D)P(D) | D(E)P(E) | D(F)P(F)
0 | A | 7,A | 3,A | ∞ | ∞ | ∞
7,A
3,A

## Slide 13
Step | Visited | D(B)P(B) | D(C)P(C) | D(D)P(D) | D(E)P(E) | D(F)P(F)
0 | A | 7,A | 3,A | ∞ | ∞ | ∞
1 | AC | 5,C |  | 11,C | 5,C | ∞
7,A
3,A
5,C
11,C
5,C

## Slide 14
Step | Visited | D(B)P(B) | D(C)P(C) | D(D)P(D) | D(E)P(E) | D(F)P(F)
0 | A | 7,A | 3,A | ∞ | ∞ | ∞
1 | AC | 5,C |  | 11,C | 5,C | ∞
2 | ACB |  |  | 9,B | 5,C | ∞
7,A
3,A
5,C
11,C
5,C
9,B

## Slide 15
Step | Visited | D(B)P(B) | D(C)P(C) | D(D)P(D) | D(E)P(E) | D(F)P(F)
0 | A | 7,A | 3,A | ∞ | ∞ | ∞
1 | AC | 5,C |  | 11,C | 5,C | ∞
2 | ACB |  |  | 9,B | 5,C | ∞
3 | ACBE |  |  | 9,B |  | ∞
7,A
3,A
5,C
11,C
5,C
9,B

## Slide 16
Step | Visited | D(B)P(B) | D(C)P(C) | D(D)P(D) | D(E)P(E) | D(F)P(F)
0 | A | 7,A | 3,A | ∞ | ∞ | ∞
1 | AC | 5,C |  | 11,C | 5,C | ∞
2 | ACB |  |  | 9,B | 5,C | ∞
3 | ACBE |  |  | 9,B |  | ∞
4 | ACBED |  |  |  |  | 10,D
7,A
3,A
5,C
11,C
5,C
9,B
10,D

## Slide 17
7,A
3,A
5,C
11,C
5,C
9,B
10,D
Step | Visited | D(B)P(B) | D(C)P(C) | D(D)P(D) | D(E)P(E) | D(F)P(F)
0 | A | 7,A | 3,A | ∞ | ∞ | ∞
1 | AC | 5,C |  | 11,C | 5,C | ∞
2 | ACB |  |  | 9,B | 5,C | ∞
3 | ACBE |  |  | 9,B |  | ∞
4 | ACBED |  |  |  |  | 10,D
5 | ACBEDF |  |  |  |  | 

## Slide 18: Now its time to understand
Flooding
Initial State
  I know my
neighbors
Final State
  I know the entire graph

## Slide 19
Lets look at the flooding demo

## Slide 21
          Link breakages are common in an network.
Link Breaking In Network
          After a link breaks, flooding in network occurs
          again and the routing tables are updated.

## Slide 22
Example
7
4
2
2
3
8
6
1
Step | Island | D(B)P(B) | D(C)P(C) | D(D)P(D) | D(E)P(E) | D(F)P(F)
0 | A | 7,A | 3,A | ∞ | ∞ | ∞
1 | AC | 5,C |  | 11,C | 5,C | ∞
2 | ACB |  |  | 9,B | 5,C | ∞
3 | ACBE |  |  | 9,B |  | ∞
4 | ACBED |  |  |  |  | 10,D
5 | ACBEDF |  |  |  |  | 
A to F

## Slide 23
Example
7
4
2
2
3
8
6
1
Step | Island | D(B)P(B) | D(C)P(C) | D(D)P(D) | D(E)P(E) | D(F)P(F)
0 | A | 7,A | 3,A | ∞ | ∞ | ∞
1 | AC | 5,C |  | 11,C | 5,C | ∞
2 | ACB |  |  | 11,C | 5,C | ∞
3 | ACBE |  |  | 11,C |  | ∞
4 | ACBED |  |  |  |  | 12,D
5 | ACBEDF |  |  |  |  | 
A to F
          Oops, the link
          broke!
          Updated!

## Slide 24: Lets look at our code And its implemented features !

## Slide 25: Router Class Functions
_complete_global_view()
forward()
receive()
_dijkstra_()
_get_shortest_path_()
_create_routing_table_()
run()
fail_link()
received_fail_link()